## Slide 1: Wireless and Mobile Network

## Slide 2: Wireless and Mobile network
Background:
# wireless (mobile) phone subscribers now exceeds # wired phone subscribers!
# wireless Internet-connected devices equals # wireline Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3: Elements of a wireless network
wireless hosts
laptop, smartphone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility
network
infrastructure

## Slide 4: Elements of a wireless network
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points
network
infrastructure

## Slide 5: Elements of a wireless network
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
network
infrastructure

## Slide 6: Elements of a wireless network
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network
network
infrastructure

## Slide 7: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 8: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET

## Slide 9: Wireless Link Characteristics (1)
important differences from wired link ….
  decreased signal strength: 무선 전파는 신호의 세기가 거리에 따라 급격하게 감소
  interference from other sources: 같은 주파수 대역을 공유하는 기술들끼리는 서로 간섭 현상을 일으킴
  다중경로전파(multipath propagation): 무선 신호는 신호를 반사하는 어떤 물체(유리 등)를 만나면 반사되어 다중 경로로 전파될 수 있음

## Slide 10: Wireless network characteristics (2)
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 11: IEEE 802.11 Wireless LAN
802.11b
2.4-5 GHz unlicensed spectrum
up to 11 Mbps
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
802.11n: multiple antennae
  2.4-5 GHz range
  up to 200 Mbps
all use CSMA/CA for multiple access
all have base-station and ad-hoc network versions

## Slide 12: 802.11 LAN architecture
The IEEE 802.11 architecture consists of several components
  BSS(Basic Service Set)
    Basic building block of an IEEE 802.11 LAN
    A set of stations that have successfully synchronized
  BSA(Basic Service Area)
    The area containing the members of a BSS
  IBSS(Independent BSS)
    STAs are able to communication directly (ad hoc network)
  DS(Distribution System)
    To interconnect BSSs
  ESS(Extended Service Set)
    An ESS is the union of the BSSs connected by a DS

## Slide 13: 802.11 LAN architecture
DS
AP
AP
STA
BSS
STA
STA
BSS
STA
ESS
Portal
Non-802.11 network
DSS
DSS
DSS
DS : Distribution System
DSS : Distribution System Service
STA : Station
BSS : Basic Service Set
ESS : Extended Service Set
AP : Access Point
AP
STA
STA
STA
IBSS

## Slide 14: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 15: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication
  will typically run DHCP to get IP address in AP’s subnet

## Slide 16: 802.11: Channels, association
Scanning
Authentication
Association
STA
Authentication Request
Authentication Response
Association Request
Association Response
AP
Association Request Format | 
Capability | 
Listen Interval | 
SSID | ‘nespot’
Supported rates | 
… | 
……
Scanning
Active or passive
Association Response Format | 
Capability | 
Status Code | 0(16 bit)
Association ID | (int)16bit
Supported rates | 
… | 

## Slide 17: 802.11: Handoff procedure
Association
Reassociation
Disassociation
AP
BSS
STA
AP
STA
BSS
STA
ESS
STA

## Slide 18: 802.11: Reassociation
The reassociation service is invoked to move a current association from one AP to another
STA
AP
Authentication Request
Authentication Response
Reassociation Request
Reassociation Response
……
New AP
Scanning
Association

## Slide 19: Super frame architecture
PCF(Point Coordination Function)
  Optional access method
  Real-time traffic
DCF(Distribution Coordination Function)
  Basic medium access protocol
  Non-real-time traffic
B
PCF
Contention-Free Period(CFP)
Contention period
DCF
Super Frame
B
Contention period
DCF
Super Frame
B
B
or

## Slide 20: Super frame architecture
AP는 DCF와 PCF 구간을 조정해서 경쟁구간과 비경쟁구간을 교대로 반복(필요시 PCF 구간 사용)
Beacon signal
  AP에 의해서 주기적으로 발생
  타이밍 정보를 관리 중인 BSS안의 노드들에게 알려주기 위함
  PCF를 알려주기 위해 사용하며 노드들은 beacon을 통해 경쟁구간인지 비경쟁구간인지 구분
DCF
  Station 간 경쟁에 의한 매체 사용 제어
  CSMA/CA 기반
  Best effort basis– no guaranteed service
PCF
  비경쟁 서비스
  AP에 의한 Polling 방식으로 매체 사용권 제거
  Time Bounded Services 제공
    낮은 전송 지연
    음성, 비디오

## Slide 21: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 22: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS(DCF inter frame space) then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS(shortest inter frame space) (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK

## Slide 23: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!

## Slide 24: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 25: DCF
A station must sense the medium before initiating the transmission of a packet
  SlotTime은 BSS 내의 왕복지연 시간
Destination
Time
Source
DIFS
RTS
CTS
SIFS
SIFS
Time
Time
Data
ACK
SIFS
NAV
Other
Contention Window
PIFS
SIFS
slotTime
DIFS
IFS : Inter Frame Space
SIFS : Shortest IFS
PIFS : SIFS + slotTime
DIFS : SIFS + 2*slotTime
Contention Window

## Slide 26: Priority Access
프레임의 중요도에 따라 IFS 에 차등을 둠
  제어용 프레임은 상대적으로 IFS 를 작게 하여 대기 시간을 줄임
  데이터 프레임, 관리 프레임을 보낼 때 : 비교적 큰 값인 DIFS
  비경쟁구간 시작시 : 그 보다 작은 PIFS
  ACK, CTS ACK, CTS 등의 제어 프레임을 보낼 때는 가장 작은 SIFS (Shortest SIFS )
By the use of IFS (Interframe Space)
  SIFS (Short IFS) : ACK, CTS, 또는 fragment
  PIFS (PCF IFS) : CFP 시작 시 priority access priority access 를 위하여 사용
  DIFS (DCF IFS) : 데이터 프레임 또는 관리 프레임을 보낼 때 사용
SIFS < PIFS < DIFS

## Slide 27: BackOff procedure for DCF
For providing Lower collision probability
  The backoff time is decreased as long as the channel is idle
  When the channel is busy, the backoff time is frozen
  After the packet collides, the backoff time increases exponentially
STA1
STA2
Frame
DIFS
Backoff
Frame
DIFS
Frame
DIFS
Frame
DIFS
Frame
Defer
Defer
Defer
Defer
= Backoff
= Remaining Backoff
STA3
STA4
STA5
Back off time = Random * slotTime
(0 Random 23+i , where i = the number of collision, 05)

## Slide 28: Point Coordination Function
Single access point controls access to the medium
  based on polling, Time-bounded service
Beacon
AP
SIFS
PIFS
STA
D1+poll
U1+ack
SIFS
D2+ack
+poll
U2+ack
SIFS
SIFS
D3+ack
+poll
PIFS
SIFS
D4+poll
U4+ack
SIFS
SIFS
CF-End
Contention-Free Period(CFP)
No response
NAV
Reset NAV
Contention period
D : down stream
U : up stream
Contention-Free Repetition Interval
Poll
Data + Poll
Data + Poll + Ack
Poll + Ack
AP
Data
Data + Ack
Ack
Null Function(no data)
STA

## Slide 29
power management
node-to-AP: “I am going to sleep until next beacon frame”
  AP knows not to transmit frames to this node
  node wakes up before next beacon frame
beacon frame: contains list of mobiles with AP-to-mobile frames waiting to be sent
  node will stay awake if AP-to-mobile frames to be sent; otherwise sleep again until next beacon frame
802.11: advanced capabilities

## Slide 30: Power Save Mode
Overview
  If an STA does not have any packet, the STA notifies the AP with the PM and switches to PSM
  When the STA is sleeping, the AP must buffer the packet
STA
AP
Frame
Control
Power
Management
1bit
NULL Data (PM = 1)
Beacon
Beacon
Frame(body)
TIM(Traffic
Indication Map)
PS Poll
Data
Management
Frame

## Slide 31
802.11: mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
switch: which AP is associated with H1?
  self-learning (Ch. 5): switch will see frame from H1 and “remember” which switch port can be used to reach H1
H1
BBS 2
BBS 1

## Slide 32: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
mobile wireless user,
using same access
point
mobile user, passing through multiple access point while maintaining ongoing connections (like cell phone)
mobile user, connecting/ disconnecting from network using DHCP.

## Slide 33: Background of mobile IP
The IP addresses are designed to work with stationary hosts because part of the address defines the network to which the host is attached.
다양한 무선 통신 기술의 등장과 함께 이동성을 지원하는 단말의 출현
  IP 네트워크에서 이동성 지원 필요성 증가
Subnet 환경이 바뀌더라도 IP 주소를 변경하지 않고 통신할 수 있도록 지원할 수 있는 기능이 필요

## Slide 34: Addressing
IP 프로토콜을 이용하여 이동통신 서비스를 제공할 때 가장 중요한 문제
정지 호스트(Stationary Hosts): netid와 subnet 주소를 이용하여 패킷 전달 가능
이동 호스트(Mobile Hosts): 새로운 네트워크에 도착 시 주소 변경->위치 식별 불가
DHCP 이용, 새로운 주소 획득
  문제점
    데이터 전송 중 일 경우 전송 중단(IP 주소가 변경됨에 따라)

## Slide 35: Components of mobile IP
Mobile IP has two addresses for a mobile host:
  home address : 영구적인 주소
  care-of address: 모바일 노드가 다른 네트워크에 접속했을 경우 변하는 주소
Agent
  호스트의 이동으로 인한 주소 변경을 다른 곳에서 알지 못하게 하기 위함
    즉, 변경한 것을 알지 못하더라도 정상적으로 데이터 송수신은 가능하게
  홈에이전트(Home agent, HA): 홈 네트워크에 연결된 라우터
  외부 or 방문 에이전스(Foreign agent, FA): 외지 네트워크에 연결된 라우터로 홈 네트워크로부터 받은 패킷을 해당 호스트에게 전달하는 역할을 함

## Slide 36: Mobility: vocabulary
wide area network
home network: permanent “home” of mobile
(e.g., 128.119.40/24)
permanent address: address in home network, can always be used to reach mobile
e.g., 128.119.40.186
home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote

## Slide 37: Mobility: more vocabulary
wide area network
care-of-address: address in visited network.
(e.g., 79,129.13.2)
visited network: network in which mobile currently resides (e.g., 79.129.13/24)
permanent address: remains constant (e.g., 128.119.40.186)
foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
Correspondent or remote host: wants to communicate with mobile

## Slide 38: Mobility: approaches
let routing handle it: routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile located
  no changes to end-systems
let end-systems handle it:
  indirect routing: communication from correspondent to mobile goes through home agent, then forwarded to remote
  direct routing: correspondent gets foreign address of mobile, sends directly to mobile
not
scalable
to millions of
mobiles

## Slide 39: 3 phase for communications
Communications between correspondent and mobile host

## Slide 40: Phase 1: Agent Discovery
이동 노드가 현재 자신이 접속해있는 네트워크를 알기 위해 사용
  홈 네트워크인지, 방문 네트워크인지
  홈 또는 방문 에이전트들은 자신의 존재를 주기적으로 브로드캐스트하여 현재 이동 노드가 접속해있는 네트워크를 알림
Mobile IP extends ICMP Router Discovery as its primary mechanism for Agent Discovery

## Slide 41: Phase 1: Agent Discovery
agent advertisement: foreign/home agents advertise service by broadcasting ICMP messages (typefield = 9)
R bit: registration required
H,F bits: home and/or foreign agent
Foreign agent only

## Slide 42: Phase 2: Registration
이동 노드가 현재 방문 중인 네트워크를 홈 네트워크에 등록하는 절차
Used to
  Request forwarding services when visiting a foreign network
  Inform their home agent of their current care-of address
  Renew a registration
  Deregister when they return home

## Slide 43: Phase 2: Registration
wide area network
end result:
foreign agent knows about mobile
home agent knows location of mobile
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent home: “this mobile is resident in my network”

## Slide 44: registration example 1
visited network: 79.129.13/24
home agent
HA: 128.119.40.7
foreign agent
COA: 79.129.13.2
mobile agent
MA: 128.119.40.186
registration req.
COA: 79.129.13.2
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 9999
identification:714
….
registration reply
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 4999
Identification: 714
encapsulation format
….
registration reply
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 4999
Identification: 714
….
time
ICMP agent adv.
COA: 79.129.13.2
….
registration req.
COA: 79.129.13.2
HA: 128.119.40.7
MA: 128.119.40.186
Lifetime: 9999
identification: 714
encapsulation format
….

## Slide 45: registration example 2
visited network: 79.129.13/24
home agent
HA: 128.119.40.7
foreign agent
COA: 79.129.13.2
mobile agent
MA: 128.119.40.186
registration req.
registration reply
time
ICMP agent adv.
COA: 79.129.13.2
….
By UDP using
the well-known port 434.
FA의 중계없이 MN이 직접 HA에게 등록 요청

## Slide 46: Data transfer via indirect routing
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent
Correspondent node

## Slide 47: Mobile IP: indirect routing
Permanent address: 128.119.40.186
Care-of address: 79.129.13.2
dest: 128.119.40.186
packet sent by correspondent
dest: 79.129.13.2
dest: 128.119.40.186
packet sent by home agent to foreign agent: a packet within a packet
dest: 128.119.40.186
foreign-agent-to-mobile packet

## Slide 48: Indirect Routing: problems
Double crossing
  Mobile host가 remote host (correspondent host)와 같은 네트워크로 이동했을 때 발생
  같은 네트워크라 직접 통신이 가능하나 지속적으로 Home agent를 거쳐 데이터를 전송

## Slide 49: Indirect Routing: problems
삼각 라우팅 (Triangle routing)
  모바일 노드가 리모트 노드와 같은 네트워크에 연결되어 있지 않는 경우 발생
Mobile node로 향하는 모든 패킷이 Home agent를 거치기 때문에 Home agent에 load가 증가
근본적으로는 home agent로 가는 모든 경로상에서 불필요한 오버헤드 증가
Mobile node의 위치에 따라 더 심각한 오버헤드를 야기할 수 있음

## Slide 50: Mobility via direct routing
1
2
3
4
home
network
visited
network
correspondent requests, receives foreign address of mobile
correspondent forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 51: Mobility via direct routing: comments
overcome triangle routing problem
non-transparent to correspondent: correspondent must get care-of-address from home agent
  what if mobile changes visited network?
1
2
3
4

## Slide 52: Accommodating mobility with direct routing
wide area network
1
foreign net visited
at session start
anchor
foreign
agent
2
4
new foreign
agent
3
correspondent
agent
correspondent
new
foreign
network
anchor foreign agent: FA in first visited network
data always routed first to anchor FA
when mobile moves: new FA arranges to have data forwarded from old FA
5

## Slide 53: Binding cache
    바인딩 요청 : CN은 MN의 위치를 알기 위해 HA에게 바인딩 요청
    바인딩 업데이트 : HA는 MN의 현 위치를 알려줌
    바인딩 확인응답 : 바인딩 업데이트 메시지를 수신한 후 응답 함
    바인딩 경고 : MN에 대한 현재의 FA가 아니라면 바인딩 경고를 송신하여 MN의 위치가 변경되었음을 알리고 새롭게 바인딩 요청을 시작
이전 FA와 새로운 FA 모두에게서 데이터를 전달받을 수 있도록 하여 Data 손실을 줄임

## Slide 54: P2P의 정보검색
분산 해시 테이블 (DHT, Distributed Hash Table)
  시스템 내의 각 노드(node)들이 키 셋을 가지고 있는 분산 시스템
  부하가 집중되지 않고 분산
  큰 규모의 노드 관리
해시 테이블
  Key = hash(original key)
Original Key | Key | Value
John Washington | 8962458 | 132-54-3570
Diana Louise Jones | 7800356 | 761-55-3791
Xiaoming Liu | 1567109 | 385-41-0902
Rakesh Gopal | 2360012 | 441-89-1956
Linda Cohen | 5430938 | 217-66-5609
……. |  | ………
Lisa Kobayashi | 9290124 | 177-23-0199
Hash
function
Key
Original Key

## Slide 55: 분산 해시 테이블: detail
DHT
  Keyspace partitioning
    분산된 peer들에게 키를 어떻게 배치시킬 것인가
  Overlaynetwork
    물리적 연결과 상관없이 완전하게 분산된 형태로 key의 위치를 찾아갈 수 있는 알고리즘을 제공
각 피어들은 key 값을 통해 데이터베이스에 쿼리(query)
  데이터베이스는 키에 해당 하는 값 (value)를 리턴
  쿼리에 해당 하는 값을 찾기 위해 적은 수의 메시지만 피어들 사이에 전송되어야 함
  각 몇몇의 피어에 대한 정보를 가지고 있음

## Slide 56: Assign key-value pairs to peers
Rule
  Key-value 쌍은 가장 가까운 ID를 가지는 peer에 할당
  가장 가까운 ID를 가지는 노드를 “다음 노드(successor)”라고 부름
e.g., ID space {0,1,2,3,…,63}
suppose 8 peers: 1,12,13,25,32,40,48,60
  If key = 51, then assigned to peer 60
  If key = 60, then assigned to peer 60
  If key = 61, then assigned to peer 1

## Slide 57: Circular DHT
1
12
13
25
32
40
48
60
each peer only aware of immediate
successor and 이전노드(predecessor).
“overlay network”

## Slide 58: Resolving a query
1
12
13
25
32
40
48
60
What is the value associated with key 53 ?
value
O(N) messages
on average to resolve
query, when there
are N peers

## Slide 59: Circular DHT with shortcuts
each peer keeps track of IP addresses of predecessor, successor, short cuts.
reduced from 6 to 3 messages.
1
12
13
25
32
40
48
60
What is the value for
key 53
value

## Slide 60: Peer churn
handling peer churn:
peers may come and go (churn)
each peer knows address of its two successors
each peer periodically pings its two successors to check aliveness
if immediate successor leaves, choose next successor as new immediate successor
example: peer 5 abruptly leaves
peer 4 detects peer 5’s departure; makes 8 its immediate successor
4 asks 8 who its immediate successor is; makes 8’s immediate successor its second successor.
1
3
4
5
8
10
12
15